## Slide 1: Fabry GT – NaCl addition at harvest
Viral Vector Pilot Plant Downstream
Biotherapeutics Process Development
08 May 2023
Andreas Maccani

## Slide 2: Background – TAK-754
TAK-754 (GT FVIII) 200L Pilot Scale (red: w/o NaCl, green: with NaCl)
 Higher harvest step yields with 128mM NaCl addition
Analysis of TAK-754 Ph1/2 Mfg batches showed significant yield differences
Six-sigma green belt project Michaela Wieshaupt  root cause analysis  impact of depth filter (Pall P900) lot-to-lot variation
Correlation of yield with Ca2+ and Mg2+ content of filter medium. Filters with Ca2+ > 130 mg/m² showed negative impact  Retention of full capsids because of higher pos. filter charge.
 Addition of NaCl to reduce AAV capsid retention in depth filter

## Slide 3: Background – Fabry GT NHP Production
TechTeam
08 Aug 2022
HAR filter setup 200L scale:
2 m² PDP8 + 2 m² V100 (Pall)
No NaCl addition
Vg step yield at HAR only around 60 – 70%
 Potential yield increase by NaCl addition

## Slide 4: Overview – TAK-028 200L Pilot Scale Production (Tox Process)
Batch ID | PFB04_2212 | PFB04_2213 | PFB04_2214 | PFB04_2215 | PFB04_2216 | PFB04_2217 | PFB04_2226 | PFB04_2227
Bioreactor FMB (200L SUB) | Pall | Sartorius | Sartorius | Pall | Sartorius | Pall | Pall | Sartorius
Transfection mix medium | FAA (DMEM) | FAB (DMEMF12) | FAA (DMEM) | FAA (DMEM) | FAA (DMEM) | FAB (DMEM/F12) | FAA (DMEM) | FAA (DMEM)
Salt addition at harvest | w/o NaCl | w/o NaCl | w/o NaCl | w/o NaCl | w/o NaCl | w/o NaCl | 135 mM NaCl | 135 mM NaCl
Comments | - | - | - | No pH dead band after transfection | - | - | - | .
Both upstream production lines (Sartorius and Pall SUBs) were used to meet the timelines.  impact on yield
Evaluation of transfection mix media DMEM low glucose (not yet qualified) and DMEM/F12 Baxter Special (qualified material)  impact on yield
Evaluation of salt addition at harvest (135 mM NaCl) to improve depth filtration step yield
  To reduce impact of filter charge (lot-to-lot variability)
Batch ID | PFB04_2212 | PFB04_2214 | PFB04_2216 | PFB04_2226 | PFB04_2227
Bioreactor FMB (200L SUB) | Pall | Sartorius | Sartorius | Pall | Sartorius
Transfection mix medium | FAA (DMEM) | FAA (DMEM) | FAA (DMEM) | FAA (DMEM) | FAA (DMEM)
Salt addition at harvest | w/o NaCl | w/o NaCl | w/o NaCl | 135 mM NaCl | 135 mM NaCl
Comments | - | - | - | - | .

## Slide 5: Vector Genome Yields (IDT ddPCR)
Batch ID | PFB04_2212 | PFB04_2214 | PFB04_2216 | PFB04_2226 | PFB04_2227
Bioreactor FMB (200L SUB) | Pall | Sartorius | Sartorius | Pall | Sartorius
Salt addition at harvest | w/o NaCl | w/o NaCl | w/o NaCl | 135 mM NaCl | 135 mM NaCl
No impact of NaCl addition on total vg yield (IDT ddPCR) visible

## Slide 6: Impurities
Batch ID | PFB04_2212 | PFB04_2214 | PFB04_2216 | PFB04_2226 | PFB04_2227
Bioreactor FMB (200L SUB) | Pall | Sartorius | Sartorius | Pall | Sartorius
Salt addition at harvest | w/o NaCl | w/o NaCl | w/o NaCl | 135 mM NaCl | 135 mM NaCl
Similar amounts of residual HEK-HCP impurities with and w/o NaCl addition
Potentially, slightly higher amounts of residual HEK-DNA with NaCl addition

## Slide 7: Ultracentrifugation (UCE)
Batch ID | PFB04_2212 | PFB04_2214 | PFB04_2216 | PFB04_2226 | PFB04_2227
Bioreactor FMB (200L SUB) | Pall | Sartorius | Sartorius | Pall | Sartorius
Salt addition at harvest | w/o NaCl | w/o NaCl | w/o NaCl | 135 mM NaCl | 135 mM NaCl
Pall runs: Shift to more full capsids with NaCl
Sartorius runs: Higher peak with NaCl

## Slide 8: Ultracentrifugation (UCE)
Batch ID | PFB04_2212 | PFB04_2214 | PFB04_2216 | PFB04_2226 | PFB04_2227
Bioreactor FMB (200L SUB) | Pall | Sartorius | Sartorius | Pall | Sartorius
Salt addition at harvest | w/o NaCl | w/o NaCl | w/o NaCl | 135 mM NaCl | 135 mM NaCl
Sartorius runs: More empty capsids with NaCl?

## Slide 9: Ultracentrifugation (UCE) – AUC
Batch ID | PFB04_2212 | PFB04_2214 | PFB04_2216 | PFB04_2226 | PFB04_2227
Bioreactor FMB (200L SUB) | Pall | Sartorius | Sartorius | Pall | Sartorius
Salt addition at harvest | w/o NaCl | w/o NaCl | w/o NaCl | 135 mM NaCl | 135 mM NaCl
AUC does not reveal a clearer picture.
Higher percentage of aggregates/overfilled capsids with NaCl
PFB04_2212 (Pall): not determined
w/o NaCl
with NaCl

## Slide 10: BDS – Vector Genome Yields
Pall SUB: approx. 40% higher vg yield with NaCl
However, no yield improvement observed with Sartorius SUB
Vg yield (200L Scale): approx. 2.0E+15 vg or 1.0E+13 vg/L harvest
Batch ID | PFB04_2212 | PFB04_2214 | PFB04_2216 | PFB04_2226 | PFB04_2227
Bioreactor FMB (200L SUB) | Pall | Sartorius | Sartorius | Pall | Sartorius
Salt addition at harvest | w/o NaCl | w/o NaCl | w/o NaCl | 135 mM NaCl | 135 mM NaCl

## Slide 11: Harvest – Step Yields
Similar cp step yields at HAR (depth filtration) – approx. 90%
However, positive trend of vg step yield observed already w/o NaCl addition (approx. 55%  73%)
Potentially, higher vg step yield with NaCl addition (>80%)
 Is there a correlation with filter medium lot (filter charge)?  Data collection in progress
ND

## Slide 12: Conclusion
  NaCl addition at harvest:
    Approx. 40% vg yield increase (BDS) observed with Pall SUB (n=1)
    However, no vg yield increase observed in Sartorius SUB runs
    No negative impact on residual HEK HCP
    Potentially, higher amount of residual HEK DNA (probably also plasmid DNA)
  Harvest vg step yield ranges from approx. 53 – 82%
    Potential impact of depth filter lot; Correlation with Ca2+ (pos. charge of filter medium)?
     Data collection in progress

## Slide 13
Questions ?